## Slide 1: FIREWALL

## Slide 2: What Is a Firewall?
Definition:
  A Network Firewall is a system or group of systems used to control access between two networks -- a trusted network and an un-trusted network -- using pre-configured rules or filters.

## Slide 3: What is a Firewall?
Device that provides secure connectivity between networks (internal/external; varying levels of trust)
Used to implement and enforce a security policy for communication between networks
Firewalls can either be hardware and/or software based.

## Slide 4: What is a Firewall?
It is the combination product that provide the function of screening routers, proxy servers, network address translation, plus stateful inspection.
Firewalls can be composed of a single router, multiple routers, a single host system or multiple hosts running firewall software, hardware appliances specifically designed to provide firewall services, or any combination thereof.

## Slide 5: What is a Firewall?
Device that provides secure connectivity between networks (internal/external; varying levels of trust)
Used to implement and enforce a security policy for communication between networks
Firewalls can either be hardware and/or software based.

## Slide 6: Firewalls History …A Brief Look
Firewall technology emerged in the late 1980s when the Internet was a fairly new technology in terms of its global use and connectivity.
The first paper published on firewall technology was in 1988, when Jeff Mogul from Digital Equipment Corporatin (DEC) developed filter systems known as packet filter firewalls.

## Slide 7: Firewalls History …A Brief Look
From 1980-1990 two colleagues from AT&T Company, developed the second generation of firewalls known as circuit level firewalls.
Publications by Gene Spafford of Purdue University, Bill Cheswick at AT&T Laboratories introduced a third generation firewall. also known as proxy based firewalls.

## Slide 8: Firewalls History …A Brief Look
In 1994 Check Point Software Technologies built readily available software known as FireWall-1.
Cisco, one of the largest internet security companies in the world released their PIX ” Private Internet EXchange ” product to the public in 1997.

## Slide 9: Network Firewall Architectures
Screening Router
Simple Firewall
Multi-Legged firewall
Firewall Sandwich
Layered Security Architecture

## Slide 10: Screening Router

## Slide 11: Simple Firewall

## Slide 12: DMZ Firewall

## Slide 13: Firewall Sandwich

## Slide 14: Layered Firewall

## Slide 15: Types of Firewalls
  Packet Filtering
  Stateful Packet Inspection
  Application Gateways/Proxies
  Adaptive Proxies
  Circuit Level Gateway

## Slide 16: Packet Filtering Firewall
A packet filtering firewall does exactly what its name implies -- it filters packets.
As each packet passes through the firewall, it is examined and information contained in the header is compared to a pre-configured set of rules or filters.
An allow or deny decision is made based on the results of the comparison.
Each packet is examined individually without regard to other packets that are part of the same connection.

## Slide 17: Packet Filtering Firewall
A packet filtering firewall is often called a network layer firewall because the filtering is primarily done at the network layer (layer three) or the transport layer (layer four) of the OSI reference model.

## Slide 18: Packet Filtering Firewall
Packet filtering rules or filters can be configured to allow or deny traffic based on one or more of the following variables:
  Source IP address
  Destination IP address
  Protocol type (TCP/UDP)
  Source port
  Destination port

## Slide 19: Packet Filtering Firewall
Advantages :
Packet filtering is typically faster than other packet screening methods.
Packet filtering firewalls can be implemented easily in a network.
They typically require no additional configuration for clients.
They can be implemented in a transparent mode.
Packet filtering firewalls are typically less expensive.

## Slide 20: Packet Filtering Firewall
Disadvantages:
Packet filtering firewalls allow a direct connection to be made between the two endpoints.
If ports are open, they are open to all traffic passing through that port, which in effect leaves a security hole in your network.
Defining rules and filters on a packet filtering firewall can be a complex task.
Packet filtering firewalls are prone to certain types of attacks. Since packet inspection goes no deeper than the packet header information

## Slide 21: Stateful Packet Inspection
Stateful packet inspection uses the same fundamental packet screening technique that packet filtering does. In addition, it examines the packet header information from the network layer of the OSI model to the application layer to verify that the packet is part of a legitimate connection and the protocols are behaving as expected.

## Slide 22: Stateful Packet Inspection Firewall
As packets pass through the firewall, packet header information is examined and fed into a dynamic state table where it is stored. The packets are compared to pre-configured rules or filters and allow or deny decisions are made based on the results of the comparison.
The data in the state table is then used to evaluate subsequent packets to verify that they are part of the same connection.

## Slide 23: Stateful Packet Inspection Firewall
This method can make decisions based on one or more of the following:
Source IP address
Destination IP address
Protocol type (TCP/UDP)
Source port
Destination port
Connection state

## Slide 24: Stateful Packet Inspection Firewall
The connection state is derived from information gathered in previous packets.
It is an essential factor in making the decision for new communication attempts.
Stateful packet inspection compares the packets against the rules or filters and then checks the dynamic state table to verify that the packets are part of a valid, established connection.
By having the ability to "remember" the status of a connection, this method of packet screening is better equipped to guard against attacks than standard packet filtering.

## Slide 25: Stateful Packet Inspection
Advantages :
Like packet filtering firewalls, have very little impact on network performance.
More secure than basic packet filtering firewalls. Because stateful packet inspection digs deeper into the packet header information to determine the connection state between endpoints.
Usually it have some logging capabilities. Logging can help identify and track the different types of traffic that pass though the firewall.

## Slide 26: Stateful Packet Inspection
Disadvantages:
Like packet filtering, stateful packet inspection does not break the client/server model and therefore allows a direct connection to be made between the two endpoints
Rules and filters in this packet screening method can become complex, hard to manage, prone to error and difficult to test.

## Slide 27: Application Gateways/Proxies
The proxy plays middleman in all connection attempts.
The application gateway/proxy acts as an intermediary between the two endpoints. This packet screening method actually breaks the client/server model in that two connections are required: one from the source to the gateway/proxy and one from the gateway/proxy to the destination. Each endpoint can only communicate with the other by going through the gateway/proxy.

## Slide 28: Application Gateways/Proxies
This type of firewall operates at the application level of the OSI model. For source and destination endpoints to be able to communicate with each other, a proxy service must be implemented for each application protocol.
The gateways/proxies are carefully designed to be reliable and secure because they are the only connection point between the two networks.

## Slide 29: Application Gateways/Proxies

## Slide 30: Application Gateways/Proxies Firewall
When a client issues a request from the untrusted network, a connection is established with the application gateway/proxy. The proxy determines if the request is valid (by comparing it to any rules or filters) and then sends a new request on behalf of the client to the destination. By using this method, a direct connection is never made from the trusted network to the untrusted network and the request appears to have originated from the application gateway/proxy.
Untrusted Network
Application Gateway (Proxy service)
Work Station

## Slide 31: Application Gateways/Proxies Firewall
The response is sent back to the application gateway/proxy, which determines if it is valid and then sends it on to the client.
By breaking the client/server model, this type of firewall can effectively hide the trusted network from the untrusted network.
It is important to note that the application gateway/proxy actually builds a new request, only copying known acceptable commands before sending it on to the destination.
Unlike packet filtering and stateful packet inspection, an application gateway/proxy can see all aspects of the application layer so it can look for more specific pieces of information

## Slide 32: Application Gateways/Proxies
Advantages:
Application gateways/proxies do not allow a direct connection to be made between endpoints. They actually break the client/server model.
Typically have the best content filtering capabilities. Since they have the ability to examine the payload of the packet, they are capable of making decisions based on content.
Allow the network administrator to have more control over traffic passing through the firewall. They can permit or deny specific applications or specific features of an application.

## Slide 33: Application Gateways/Proxies
Disadvantages:
The most significant weakness is the impact they can have on performance. It requires more processing power and has the potential to become a bottleneck for the network.
Typically require additional client configuration. Clients on the network may require specialized software or configuration changes to be able to connect to the application gateway/proxy.

## Slide 34: Circuit-level Gateway
Unlike a packet filtering firewall, a circuit-level gateway does not examine individual packets. Instead, circuit-level gateways monitor TCP or UDP sessions.
Once a session has been established, it leaves the port open to allow all other packets belonging to that session to pass. The port is closed when the session is terminated.
circuit-level gateways operate at the transport layer (layer 4) of the OSI model.

## Slide 35: Linux Firewall
Any command or configuration file that is configured to block data from coming into your system or LAN is a firewall.
The Linux has 2 built-in firewalls Ipchains and Iptables.
Iptables is easy to configure and manage thus widely used.
Iptables commands are connected in chains.
Each command is used to block or allow data associated with specific protocol.

## Slide 36: Configuring Iptables
The Iptables command is based on regulating data traffic in 3 directions
      In
      Out
      Through
You can configure Iptables to stop data from coming in from an outside network.
You can configure Iptables to stop data from going out.
And you can configure Iptables to regulate data that is forwarded.

## Slide 37: Configuring Iptables
3 default chains that control all traffic to flow through the firewall
INPUT
FORWARD
OUTPUT
Along with these predefined chains users can define their own chains also.
You can define rules to block or allow data in one of these chains or can create your own chain.
The Other 2 chains are
PREROUTING
POSTROUTING

## Slide 38: Configuring Iptables
The Iptables command format is as follows
Iptables –t table option pattern –j target
The –t table option tells which table to use.
3 basic tables are available :-
Filter
NAT
MANGLE
The NAT table supports network address translation
The filter table allows you to block or allow specific types of network traffic

## Slide 39: Configuring Iptables
The mangle table rules allow modifications to packets.
Options for Iptables
-A chain rule appends a rule to the end of a chain
-D chain number deletes the rule number from a chain
-F chain flushes or deletes all rules in a chain
-I chain number rule inserts a rule in a chain with the specified rule number
-L chain lists the current rules in the chain
-N chain starts a new chain
-X chain deletes a user defined chain

## Slide 40: Configuring Iptables
The Iptables –L command lists all of the current rules on all chains.
Eg of Iptables command
# iptables –A FORWARD –p icmp –icmp-type echo-request –m limit –limit 1/s –j ACCEPT
The above command appends a limit of a packet every second to the ping command that is forwarded through your computer thus preventing the ping of death attack.

## Slide 41: Configuring Iptables
Switches for Iptables
--dport port
specifies the destination TCP/IP port number
--icmp-type message
Allows you to specify the type of icmp message echo-request is a message sent by a ping command
-j action
Defines the action to be taken if the rule of the command is satisfied normally ACCEPT, DROP, REJECT or LOG
--limit time
Sets an allowable rate for a specific message. Can be in seconds, minutes, hours or days. Eg 2/s = 2 per second

## Slide 42: Configuring Iptables
-m condition
Looks at the data for a match maybe a protocol such as TCP or UDP or a condition such as a limit.
-p protocol
Checks the data for a specific protocol such as TCP or UDP
-s ip address
Specifies a source ip address
--sport port
Sets a source TCP/IP port

## Slide 43: Configuring Iptables
--tcp-flags fl1,……
Looks for specified flags in a TCP packet
  SYN packets are sent from a client & expect a reply
  ACK packets acknowledge SYN request
  FIN the final packet in a communication
  RST packets tell a client that a request has been rejected

## Slide 44: Configuring Iptables
Actions for Iptables
-j ACCEPT
Allows packets that match the specified rule into, out of, or forward through the firewall
-j DROP
Stops the packet that match the specified rule without informing the source
-j REJECT
Stops packets that match the specified rule with an error to the source
-j LOG
Logs a of the matching packet in /var/log/messages

## Slide 45: Configuring Iptables
! The exclamation mark is used to tell Iptables of the exceptions in a rule
Some examples of Iptables command
Iptables –A FORWARD –s 192.168.10.1 –p icmp –j ACCEPT
Iptables –A FORWARD –s !192.168.10.1 –p icmp –j ACCEPT
Iptables –A FORWARD –s 192.168.10.0/24 –p icmp –j ACCEPT
Iptables –I test –p tcp –m tcp –dport 80 –tcp-flags SYNC,RST,ACK SYN –j ACCEPT

## Slide 46: Configuring Iptables
Saving configuration changes
The firewall configuration is saved to
/etc/sysconfig/iptables
To save the changes the command is
# service iptables save
To start the firewall the command is
# service iptables start

## Slide 47: Configuring Iptables
Setting up IP Masquerading
Ip Masquerading allows you to hide the ip address of the computers on your LAN.
It replaces these ip addresses with the public ip address of your gateway
Eg
Iptables –t nat –A POSTROUTING –s 192.168.10.0/24 –o eth0 –j MASQUERADE